Vivante NPU driver

---
What is it?
- Accelerator for convolution neural networks (CNNs)
- IP closely based on Vivante GPUs
  - 1 GPGPU programmable core
  - 4 tensor processing cores
  - 8 convolution cores (64x64 systolic arrays of multiply-accumulate units)
- Found in SoCs from Amlogic, Rockchip, NXP, Synaptics, …
- Present in SBCs such as LibreComputer’s Cottonwood Alta

---
Current status
- TensorFlow Lite delegate as Mesa front-end/state tracker (Teflon)
- Passes a description of a model’s operations to Gallium drivers
- Etnaviv implements operations for a few convolution variants
  - Those that the fixed-function HW supports
  - Tensor transformations currently (naively) performed in the CPU
- Other operations are offloaded to the CPU by TensorFlow Lite (XNNPACK delegate on Arm CPUs)

---
Current status (cont.)
- MobileNetv1 (2017) at full accuracy and full (224x224) resolution:
  - CPU (XNNPACK): ~100 ms.
  - Blob: ~8 ms.
  - Etnaviv: ~34 ms.
    - 21 ms. transforming input
    - 12 ms. running the job on the NPU
    - 1 ms. transforming output

---
Short term work
- Upstream all the stuff!
  - 2 small kernel patches sent but not merged yet
  - Some cleanups still needed in the Mesa draft MR + CI job
- Performance:
  - Do tensor transformations on the TP cores
  - Store intermediate tensors in SRAM (dmabuf heaps)
  - Compress zero coefficients in sparse weight tensors
  - Skip zero coefficients
  - I’m confident we will get close to the blob’s performance

---
Longer term work
- Support operations used in more modern models with the programmable core
  - By generating CL-like kernels inside the Gallium driver
- Implement NN HAL as a state tracker? PyTorch Mobile? ONNX?
- Drivers for other HW?
  - Qualcomm, Imagination, Arm, Rockchip, Mediatek, Amlogic, TI, etc.

---
Questions
You can ask in #ml-mainline at OFTC